## Slide 1
Multi-Agent Flood Early-Warning
Intelligence Platform
AI-orchestrated · GIS-native · Built entirely on official open data
Briefing for the Chairman, National Disaster Management Authority
Prototype v1 · July 2026 · NDMA Technical Team
Notes: Open with the 2022 floods: 33 million affected. The question this project answers — can we see the next one coming, for any district of Pakistan, automatically?

## Slide 2
The problem we set out to solve
2010
Superflood — ~2,000 lives lost, 20M affected. Marala Headworks passed ~260,000 cusecs.
2022
Monsoon floods — 33M affected, $30B+ damage. One-third of the country inundated.
Today
Flood intelligence is fragmented: rainfall, river flows, terrain and population sit in separate systems, joined manually under pressure.
Decision-makers need ONE screen that fuses rainfall, river forecasts, terrain and exposure into a single, defensible risk assessment — for ANY basin, province or district — in minutes, not days.
Notes: Emphasize the manual-fusion pain point — every number in the room today comes from a different office.

## Slide 3
What we built
4+1
Specialist agents
Weather · River · Terrain · Exposure, orchestrated by a Coordinator that issues the decision.
130
Areas of interest
5 river basins + 6 provinces + 119 districts — one dropdown drives the entire system.
0–100
Rule-based risk score
Transparent weighted fusion → NDMA-style decision ladder. No black box.
100%
Official open data
NASA · NOAA · Copernicus · USGS · WorldPop. Zero data cost, full licence compliance.
Full-screen WebGIS
Dark glass UI · agent-wise layer control · province/district rain choropleths with on-map values · draggable legend · measurement & drawing tools · live station markers coloured by FFD flood category.
Automatic reporting
Every assessment produces a full situation report — saved locally as Markdown + JSON with complete provenance (every number traceable to its agent), plus a browsable report history.
Notes: This slide is the 30-second version. Everything after it is proof.

## Slide 4
Live demonstration — 3 minutes
1 · Select AOI
(e.g. Chenab or any district)
2 · Map loads
terrain, rivers, rain, boundaries
3 · Run pipelines
🌧️ 🌊 ⛰️ 👥 independently
4 · Full risk
score · decision · conversation
5 · Report
💾 saved with one click
Pipeline | What the Chairman sees | Typical time
🌧️ Weather | Observed 24/72 h + forecast 72 h rain cards (mean & max, data latency shown) | 4–13 s
🌊 Disaster | Stations recolour by FFD flood category; worst station named | 3–35 s
⛰️ Terrain / 👥 Exposure | AOI area · population & floodplain population | 2–3 s (cached)
⚖️ Full risk | Banner: LOW 0/100 → routine monitoring · agent conversation · report | ~25 s
Notes: Have localhost:5000 open in the next tab. If internet fails: cached Chenab run still works end-to-end.

## Slide 5
Data foundation — every number has an official source
Domain | Source (owner) | Resolution | Update cycle | Why chosen
🌧️ Observed rain | GPM IMERG V07 (NASA) | ~11 km, 30-min | 1–3 day latency, shown in UI | Global standard; sees whole basin incl. upstream catchments outside Pakistan
🌦️ Forecast rain | GFS 0.25° (NOAA) | ~28 km | 4 runs/day | Open operational NWP; latest run auto-selected
🌊 River discharge | GloFAS (Copernicus EU) | 0.05°, to +120 h | Daily cycle | Only free operational discharge forecast covering the entire Indus system
⛰️ Terrain | SRTM 30 m (NASA/USGS) + HydroSHEDS (WWF) | 30/460 m | Static | Reference global DEM + hydrology derivative
👥 Population | WorldPop 100 m (Univ. Southampton) | 100 m | 2020 baseline | Humanitarian-planning standard (UN OCHA, WHO)
🗺️ Boundaries | FAO GAUL 2015 L1/L2 | 500 m simplified | Static | Official UN admin layers; disputed areas handled explicitly
Classification: Pakistan FFD flood-limit bands (cusecs, per station) · Total data cost: $0 · Sources documented in code headers
Notes: If asked why not PMD data: PMD publishes no machine-readable API; these are the automatable official equivalents, and outputs are verified against FFD/PMD bulletins, not replacing them.

## Slide 6
System architecture
Browser WebGIS
Leaflet · vanilla JS
presentation only
⇄
Flask API
12 JSON endpoints
thin — zero analysis logic
⇄
Agent layer
ALL logic lives here once
weather · river · terrain
population · coordinator
report · AOI resolver
⇄
External services
Google Earth Engine
Copernicus EWDS
Anthropic (warning text only)
Separation of concerns
Measurement (4 deterministic agents) · Judgement (rule-based coordinator) · Language (LLM, wording only). Each layer independently testable and replaceable.
Compute where the data lives
Heavy geoprocessing (zonal stats, terrain) runs on Google's Earth Engine servers — our machine only orchestrates. Batched calls: 1–2 round-trips per agent.
Two frontends, one brain
Streamlit for internal iteration; Flask + Leaflet WebGIS for operations. Both call the same agent modules — logic exists exactly once.
Notes: The architecture question WILL come from the AI researchers — the answer is the measurement/judgement/language separation.

## Slide 7
The specialist agents
🌧️ Weather
In: AOI geometry
Out: 24/72 h observed + 72 h forecast rain (AOI mean & max), data latency
Windows anchor to newest satellite image — staleness is measured, never hidden
🌊 River
In: in-AOI stations + weather's rain outlook
Out: discharge per station (+24…+120 h) in FFD categories; worst station
Channel-snapping window fixes grid offsets
⛰️ Terrain
In: AOI geometry
Out: DEM, slope, flow-accumulation GeoTIFFs + AOI area
Static — computed once per AOI, cached forever
👥 Exposure
In: AOI geometry
Out: total + floodplain population (slope<2° proxy)
e.g. Chenab: 69.1M total, 51M floodplain
COORDINATOR resolves the AOI once, runs the four specialists, hands the weather agent's rain outlook to the river agent as context, logs every hand-off into an auditable conversation, fuses components into the score and decision — then commissions the report.
Notes: Point out the genuine data hand-off (weather→river): agents talk with real numbers, not theatre.

## Slide 8
Agents talk — and the conversation is evidence
coordinator → all agents: New assessment for AOI 'chenab'. Resolving geometry and in-AOI FFD stations.
coordinator → terrain: Prepare static terrain layers for Chenab basin.
terrain → coordinator: Layers ready. AOI area 88,788 km²; DEM/slope/flow-accumulation cached.
weather → river: Rain outlook for your discharge context: 10.9 mm fell (72 h basin mean, 32 h latency); 11.5 mm forecast next 72 h.
river → coordinator: Worst station Trimmu: normal (1,417 m³/s peak over 120 h horizon).
coordinator → decision: Components {river: 0, rain_forecast: 0, rain_observed: 0} → score 0/100 (low).
decision → report: Generate the situation report.
Every message is generated by rules from the real numbers — no LLM — and stored in the saved JSON. The full reasoning chain of any warning can be audited months later.
Notes: This is a real conversation log from a live run — not an illustration.

## Slide 9
One selector, any geography
"chenab"
river basin (HydroBASINS union)
"province:Punjab"
GAUL level-1
"district:Multan"
GAUL level-2
→ AOI resolver → everything
geometry · cache key · in-AOI FFD stations · GloFAS window → layers, outline, pipelines, risk, report
▪ Stations follow geography: a district's river assessment uses whichever gauged FFD stations physically fall inside its polygon — verified spatially, not assumed.
▪ Honest gaps: a district with no gauge runs in DEGRADED mode — the river component is dropped and declared, never fabricated.
▪ Rain choropleths are clipped to the AOI with values printed on each polygon — provincial and district forecast maps answer NDMA's "who gets how much rain, where" directly.
Adding a new AOI is a registry entry — NOT new code. All 119 districts of Pakistan work today.
Notes: GIS engineers will probe the district-station logic — answer: EE point-in-polygon at resolve time, one batched call.

## Slide 10
Risk fusion — transparent, reproducible, rule-based
River · weight 0.5
Worst-station FFD category
normal 0 → low 30 → medium 50 → high 70 → very high 90 → exceptional 100
Forecast rain · 0.3
GFS 72 h AOI-mean (mm)
≥25→20 · ≥35→40 · ≥50→60 · ≥70→80 · ≥90→100
Observed rain · 0.2
GPM 72 h AOI-mean (mm)
same calibrated steps
score = Σ weightᵢ · componentᵢ / Σ weightᵢ (failed agents dropped, weights renormalised, "degraded" flagged)
< 20 · LOW
routine monitoring
< 40 · MODERATE
advisory to PDMA/districts
< 60 · HIGH
flood alert · pre-position teams
≥ 60 · SEVERE
flood warning · activate response
Anyone in this room can recompute the score from the report tables with a calculator. That is deliberate.
Notes: The decision ladder mirrors NDMA's advisory→emergency escalation, so outputs drop into existing SOPs.

## Slide 11
Calibrated on Pakistan's own flood history
~100 mm
2010 superflood — peak 72 h basin-mean rainfall (GPM backtest, Chenab)
~51 mm
2022 floods — clearly separated from the non-flood baseline
~34 mm
2018 ordinary monsoon (control) — correctly stays LOW
▪ Rain thresholds were rejected and recalibrated when the first metric (basin-max) failed the 2018 control — the system is tuned to discriminate, not to alarm.
▪ Discharge backtest ranks 2010 > 2022 ≈ 2018 correctly, and quantified a real bias: GloFAS runs ~2× low vs FFD-reported flows (2010 Marala: GloFAS ~114k vs ~260k reported cusecs).
▪ That bias is printed as a caveat in every report: river categories are conservative until per-station correction lands. We publish our known weaknesses.
Validation artefacts are reproducible scripts in the repo — hydrologists can rerun them today.
Notes: Finding and documenting the GloFAS bias is a credibility asset, not a weakness — lead with it before anyone asks.

## Slide 12
Cross-validated against an independent commercial provider
The test
Meteoblue 'precip today' map for 08 Jul 2026 (23 rainfall bands, 1–90 mm, ~4 km multi-model) compared zonally against our NASA GPM (observed) and NOAA GFS (forecast) for the same day.
The result
Within Pakistan, all three products agree: a light-rain day (≤12 mm) — matching the dashboard's live values. Spatial rank correlation 0.5–0.7: where Meteoblue paints more rain, our data shows more rain.
Apparent difference | Verified explanation
Meteoblue's heavy bands (12–90 mm) missing from our AOIs | 0% of those bands lie inside Pakistan — they are in India (76–79°E); no Pakistani AOI is affected
Meteoblue peaks sharper than GFS | ~4 km model resolves local convection that a 25 km global model smooths — a model-resolution property, not an error
Satellite (GPM) totals lower | Observed day was 18/48 images published at check time — the exact 1–3 day latency the UI already displays
Every difference between our data and an independent provider is explainable, quantified, and already disclosed on-screen.
Notes: Run 09 July against Meteoblue's 08-Jul precipitation map (23 rain bands, 1-90 mm). The check scripts are reproducible. Key line: differences are explainable and disclosed — that is what data integrity looks like.

## Slide 13
Where AI is — and where it is not allowed
Step | AI? | Why
Data acquisition (4 agents) | No — deterministic code | Numbers must be measurements
Risk score · level · decision | No — fixed rules | Must be reproducible & auditable
Agent conversation log | No — rule-generated | Evidence, not narrative
Situation report | No — template over computed values | Every figure traceable
Public warning wording | YES — one LLM call (Anthropic) | Phrasing only; forbidden to invent/change/recompute any figure; template fallback if offline; operator reviews before dissemination
No AI system ever produces a NUMBER or a DECISION on this platform. Hallucination is prevented BY ARCHITECTURE — not by hoping the model behaves.
Notes: This is the single most important slide for leadership trust. Pause on it.

## Slide 14
Reporting — automatic, local, fully traceable
Generated after every decision
• Assessment & decision table · component scores
• Per-station discharge in m³/s AND cusecs
• Rainfall tables with data latency · exposure · explicit caveats
• Saved automatically to data\reports\ as Markdown + JSON, filename = AOI + timestamp — nothing overwritten, history accumulates
Operator workflow
• 💾 Save report button re-saves the on-screen assessment without re-running agents
• Report history panel — any past report opens in one click (MD or JSON)
• The JSON twin holds every agent output and the full conversation — a warning issued today can be reconstructed exactly, months later
Reproducibility standard: same inputs → same score → same decision → same report. An inquiry can replay any assessment.
Notes: Show a saved sitrep briefly — the caveats section demonstrates institutional honesty.

## Slide 15
Engineered for failure — degraded, never wrong
Graceful degradation
• Agent failure → component dropped, weights renormalised, DEGRADED stamped on banner & report with the failed agent named
• Zero usable data → decision = manual_review. The system never guesses.
• GloFAS not yet published → automatic fallback to yesterday's cycle
• Satellite latency → measured and displayed, not hidden
• LLM offline → deterministic template text; assessment unaffected
Caching — only what cannot change
• Terrain rasters, population totals → static datasets (delete file to refresh)
• GloFAS NetCDF → keyed by forecast date; a day's forecast never changes
• Map tile URLs → 2 h TTL (URLs, never data)
• LIVE RAIN & DISCHARGE STATS → never cached, recomputed every run
Final audit before this briefing: 18/18 end-to-end checks · 7/7 unit tests · all five pipelines verified live on basins, provinces and districts.
Notes: If internet dies mid-demo: static layers still render, dynamic agents fail loudly and correctly — which itself demonstrates the design.

## Slide 16
Limitations — stated before you ask
Limitation | Impact | Planned fix
GloFAS ~2× low vs FFD flows | River categories conservative (under-warn) | Per-station bias correction or return-period thresholds
Non-Chenab FFD bands unverified | Category boundaries approximate | Manual verification against ffd.pmd.gov.pk (site blocks automation)
Floodplain = slope<2° proxy | Exposure indicative, not for evacuation planning | Sentinel-1 SAR inundation mapping
No flash-flood / coastal / urban drainage | Riverine floods only | Out of GloFAS scope — additional agents later
Rain thresholds calibrated on Chenab only | Other basins reuse steps | Per-basin backtests (script exists)
Observed rain lags 1–3 days · exposure is 2020 baseline | Quantified & displayed | IMERG Early Run · newer WorldPop
Every one of these is also printed inside the generated reports. A tool that hides its weaknesses cannot be trusted with warnings.
Notes: Volunteering limitations first disarms the hardest questioners — the hydrologists already know most of these.

## Slide 17
Roadmap to nationwide operations
Phase 1 · Hardening
Verify all FFD bands · GloFAS bias correction · per-basin calibration
~weeks
Phase 2 · Automation
Scheduled 6-hourly runs, all 119 districts · PostGIS + object storage · production WSGI
~1–2 months
Phase 3 · Dissemination
SMS/email alert hooks on the decision ladder · operator review SOP · PDMA dashboards
with NDMA IT
Phase 4 · Expansion
Sentinel-1 inundation agent · snowmelt (MODIS) · reservoirs · damage estimation
continuous
Why it scales
Heavy compute already runs on Google's infrastructure; our servers only orchestrate. Nationwide = registry entries + a scheduler, NOT new architecture.
Operating cost
Data $0 (all open licences) · Earth Engine research tier · pennies of LLM per assessment (optional). Cost is people, not licences.
New hazards plug in
Every future capability is just another agent with the same contract: JSON out, conversation in, weight in the fusion.
Notes: The ask comes next — this slide shows the money and effort are modest and front-loaded on verification.

## Slide 18
Five pipelines. Official data only.
Rules decide — AI only speaks.
What exists today
Working end-to-end for every basin, province and district — validated against 2010/2022/2018, fully documented, audited 18/18.
What we ask
Endorse a monsoon-season operational pilot: FFD band verification support, 2–3 districts + Chenab, alongside existing procedures.
What Pakistan gets
A defensible, explainable, sovereign early-warning capability — built on free data, owned by NDMA, expandable hazard by hazard.
Technical annexes: docs/ARCHITECTURE.md · docs/PRESENTATION_QA.md · live system at localhost:5000
Notes: End on the pilot ask. Then open the WebGIS and take questions on the live system.